## Slide 1
Planning Clocking Domains for Dante, Q-LAN and AES67

## Slide 2: Precision Time Protocol (IEEE-1588)
PTP v1 (1588-2002)
Dante
QLAN
AES67
PTP v2 (1588-2008)
Requires multicast on network
Utilizes a process called election to determine Master / Preferred Leader
  Happens each time a device is added to the network
Extremely sensitive to Jitter on network
QoS protects PTP packets on network
Not backwards compatible
  Requires use of Boundary Clock devices

## Slide 3: Clocking Scenarios

## Slide 4: Scenario 1: Standalone Cores
Equipment:
2x Core 110f
No network audio peripherals

## Slide 5: Scenario 1: Standalone Cores
Only Inventory item is Core and Softphone

## Slide 6: Scenario 1: Standalone Cores
No PTP clocking is needed, so no clock is generated
Core-1
Core-2
Primary Leader Clock: None
Notes: -Roughly 7.2 enabled this feature
-Force on via Design Properties

## Slide 7: Scenario 2: Q-LAN Peripherals
Equipment:
2x Core 110f
  1x I/O-8 Flex per Core

## Slide 8: Scenario 2: Q-LAN Peripherals
PTPv2 – Domain 0
BMCA Determines Clock Leader
  With Defaults, Lowest MAC Wins Election
Core-1
Core-2
Flex-1
Flex-2
Primary Leader Clock: Core-1

## Slide 9: Scenario 3: Q-LAN Peripherals with Priority
Equipment:
2x Core 110f
  1x I/O-8 Flex per Core

## Slide 10: Scenario 3: Q-LAN Peripherals with Priority
PTPv2 BMCA Algorithm:
  Priority 1
  Class
  Accuracy
  Variance
  Priority 2
  UID (MAC Address)
Lowest Priority Wins
Q-SYS Defaults are:
  PTP Priority 1: 254
  PTP Priority 2: 100

## Slide 11: Scenario 3: Q-LAN Peripherals with Priority
PTPv2 – Domain 0
Core 2 won BMCA based off Priority 1 Value (100) vs Core 1 (254)
Core-1
Core-2
Flex-1
Flex-2
Primary Leader Clock: Core-2

## Slide 12: Scenario 4: Q-LAN Alternate Domains
Equipment:
2x Core 110f
  1x I/O-8 Flex per Core

## Slide 13: Scenario 4: Q-LAN Alternate Domains
Domains allow multiple clocks to exist on the same network
  All Q-LAN devices in Design are assigned to the same domain
Q-LAN Tx/Rx, System Link, and AES67 Tx/Rx between two cores require them to be in the same domain
All Dante devices are in Domain 0 unless DDM is utilized
Notes: -No QLAN audio between Cores

## Slide 14: Scenario 4: Q-LAN Alternate Domains
Each Core is in Separate Clocking Domain and its own Leader
  Peripherals Clock to each Core’s domain
PTPv2 – Domain 1
PTPv2 – Domain 0
Core-1
Core-2
Flex-1
Flex-2
Primary Leader Clock: Core-1 and Core-2
Notes: -No QLAN audio between Cores

## Slide 15: Scenario 5: Dante Device in AES67 Mode
Equipment:
2x Core 110f
  1x I/O-8 Flex per Core
1x unD6IO-BT – AES67 Enabled (Ultimo X)
1x Legacy unDX4I (Ultimo)

## Slide 16: Scenario 5: Dante Device in AES67 Mode
Enabling AES67 turns on PTPv2 Clock on Dante Devices
Devices with AES67 enabled still utilize PTPv1 for synchronization with other Dante devices
All Dante Devices are in Domain 0 unless DDM is utilized
Boundary Clocks bridge PTPv1 and PTPv2 domains
Notes: -No QLAN audio between Cores

## Slide 17: Scenario 5: Dante Device in AES67 Mode
PTPv1 – Domain 0
PTPv2 – Domain 0
unD6IO-BT is Clock Leader and Boundary Clock for both PTPv1 and PTPv2
BC
unDX4I
Core-2
unD6IO-BT
Flex-2
Core-1
Flex-1
Primary Leader Clock and Boundary Clock: unD6IO-BT

## Slide 18: Scenario 6: Modify PTP1 Priority
Equipment:
2x Core 110f
  1x I/O-8 Flex per Core
1x unD6IO-BT – AES67 Enabled (Ultimo X)
1x Legacy unDX4I (Ultimo)

## Slide 19: Scenario 6: Modify PTP1 Priority
To have a Core be Preferred Leader, set the PTP Priority 1 less than 127 and ensure no Preferred Leader selected

## Slide 20: Scenario 6: Modify PTP1 Priority
PTPv1 – Domain 0
PTPv2 – Domain 0
unD6IO-BT is Boundary Clock
BC
unDX4I
Core-2
unD6IO-BT
Flex-2
Core-1
Flex-1
Primary Leader Clock: Core-1

## Slide 21: Scenario 7: Software Based Dante
Equipment:
2x Core 110f
  1x I/O-8 Flex per Core
  Software Based Dante
1x unD6IO-BT – AES67 Disabled (Ultimo X)
1x Legacy unDX4I (Ultimo)

## Slide 22: Scenario 7: Software Based Dante
Software Based Dante enabled PTPv1 and PTPv2 Clock on Core
PTP Domain only applies to PTPv2 Devices
  Must use DDM to change PTPv1 Domain
Core acts as Boundary Clock between PTPv1 and PTPv2 Domain
Unable to run separate PTPv1 and v2 Clocking
  Requires hardware Dante card in Frame or 510i

## Slide 23: Scenario 7: Software Based Dante
PTPv1 – Domain 0
PTPv2 – Domain 0
Default PTP Priority in Core prevents it from winning BMCA
BC
Primary Leader Clock: unD6IO-BT
unDX4I
Core-2
unD6IO-BT
Flex-2
Core-1
Flex-1

## Slide 24: Scenario 8: Software Based Dante with PTP Priority
Equipment:
2x Core 110f
  1x I/O-8 Flex per Core
  Software Based Dante
1x unD6IO-BT – Disable AES67 (Ultimo X)
1x Legacy unDX4I (Ultimo)

## Slide 25: Scenario 8: Software Based Dante with PTP Priority
To have a Core be Preferred Leader, set the PTP Priority 1 less than 127 and ensure no Preferred Leader selected

## Slide 26: Scenario 8: Software Based Dante with PTP Priority
PTPv1 – Domain 0
PTPv2 – Domain 0
BC
Primary Leader Clock and Boundary Clock: Core-1
unDX4I
Core-2
unD6IO-BT
Flex-2
Core-1
Flex-1

## Slide 27: Real World Scenarios

## Slide 28: Meeting Room

## Slide 29: Paging System

## Slide 30: Campus Building
Classroom 101
Classroom 102
Classroom 103
Auditorium
Building PA System
Remote Input for Events

## Slide 31: Recap
PTP v1 (1588-2002)
Dante
QLAN
AES67
PTP v2 (1588-2008)
Planning Clocking is Important Part of the Design Process
PTP Domains can be used to break up clocking within a subnet
PTP Priority can be used to influence clock election
Software-based Dante allows for Core to be both PTPv1 and v2 Leader

## Slide 32
Questions?