## Slide 1: Q-SYS and Dolby Atmos: cinema audiovisual solutions

## Slide 2: What IS Immersive Sound?
A sonic environment created in the theatre intended to “immerse” the audience more deeply into the visual experience on the screen
Create a realistic sound field relative to the image on screen
Hemispherical sound coverage
    Front, sides, rear, overhead
Sometimes called “3D Sound”

## Slide 3: Channel-based
  Traditional method used in music and cinema sound mixing
  Content is mixed to one or more channels (left, center, right or some combination via standard panning techniques)
  Each channel is the content delivered to one or more loudspeakers (for surround)

## Slide 4: Object-based
  Sound elements in the mix are bundled with location metadata to form “objects”
  Objects can be positioned virtually anywhere within the existing loudspeaker sound field

## Slide 5: Dolby Atmos
Introduced in 2012
More than 6,000 screens installed or committed
Object-based
Allows up to 128 audio tracks plus associated metadata to be rendered in real time and distributed to up to 64 loudspeakers
Specific in-theatre system design guidelines enforced by Dolby
Requires Dolby CP-850 processor or IMS-3000 IMB for each theatre

## Slide 6: Implications for Audio Systems
More loudspeakers
Full-range surround capability
More amplifier channels (1 per surround)
More power per amp channel (surrounds need to play louder)
More channels of signal processing
5.1/7.1
Immersive

## Slide 7: Implications for Audio Systems Loudspeakers
Requires many more loudspeakers
Requires high output surround loudspeakers
  One loudspeaker may need to cover nearly the entire room
Structural integrity
  Overhead installation
Aiming flexibility
  Atmos spec has specific position and aiming requirements
Installable LFE for surrounds
  Surround tracks may have Low Frequency or subwoofer content

## Slide 8: Surround Loudspeakers SR-1290 & SR-1590
Safe Installation is a key consideration

## Slide 9: Surround Loudspeakers SR-1290 & SR-1590
Safe Installation is a key consideration
15mm plywood construction and internal bracing enhances structural integrity for safe, secure installation in overhead applications
Safety Eyebolt included

## Slide 10: Surround Loudspeakers SR-5152
Very high output
Ideal for near-screen or very high ceilings in Dolby Atmos installation

## Slide 11: Surround Loudspeakers SR-5152
Very high output
Ideal for near-screen or very high ceilings in Dolby Atmos installation
15mm plywood construction
4-hole mounting points accept multi-axis wall mount bracket
Safety Eyebolt included

## Slide 12: Subwoofers
Ceiling-mounted subwoofers may be required to enhance surround LFE
QSC SB-118f and SB-218f

## Slide 13: Implications for Audio Systems Signal Processing
Signal routing is much more complex
  Especially with object-based formats
Need for significant amount signal processing power
  Loudspeaker equalization and timbral matching is much more complex
  Delay in large rooms
Q-Sys is QSC’s digital audio networking platform for control, processing, monitoring, and signal distribution

## Slide 14: Implications for Audio Systems Amplification
Cinema immersive audio systems can be very large.
Multi-channel networked amplifiers are recommended
  Reduces system complexity, rackspace, wiring, power requirements
  Allows for remote monitoring and control

## Slide 15: Required Dolby Hardware
Dolby CP850 Cinema Processor with Atmos Enablement License
Dolby IMS3000 Integrated Media Server with Atmos Enablement License
or
Available from authorized Dolby cinema equipment dealer

## Slide 16: Required Q-SYS Hardware
Core Nano/8 Flex or,
Core 110c/f or,
Core 510c/i
QLAN Network Switch
DPAQ/CXQ Amplifiers

## Slide 17: Required for Pre-Authorization
Completed Dolby Atmos Room Design Tool: DARDT*
Architectural drawings with loudspeaker locations and aiming**
*Contact you QSC sales director for questions about available professional services.
**Provided by system integrator or architect.
Documentation required by Dolby for pre-approval of the Atmos system:

## Slide 18: Q-SYS Design
The Q-SYS design is critical for proper gain staging and system equalization.
  Contact your QSC sales director for QSC professional design service options.

## Slide 19: Commissioning
Must be completed prior to receive final approval from Dolby.
  Atmos KDM’s only available for approved Atmos systems.
Must be completed by Dolby authorized commissioning engineer.
  Commissioning services available directly from Dolby or from authorized 3rd party Dolby partner/dealer.
Atmos commissioning report must be completed and submitted to Dolby for final approval.

## Slide 20: Atmos Case 1.a
This Is the simplest scenario. It is composed of:
Dolby CP850 Processor
Core 110C
Two Networks (Two Switches or one Managed switch with separated VLAN’s)
DPA Q Amplifiers (Up to 64 channels)
Q-Sys
Management

## Slide 21: Atmos Case 1.c
In this scenario the Dolby CP850 is integrated Into the IMS3000 media server. There is a configuration page for the AES67 within the Web UI. It is composed of:
IMS3000
Core 110C or 510c
Two Networks (Two Switches or one Managed switch with separated Vlans)
DPA Q Amplifiers (Up to 64 channels)
Q-Sys
Management

## Slide 22: DPA-Q Network Amplifier
4 and 8-channel amplifiers
Complete networked system using Q-Sys

## Slide 23: DPA-Q and Immersive Systems
Example system using DPA-Q amps and Q-Sys
Dolby CP850
Core 110c
NS-1124P

## Slide 24: DPA-Q and Immersive Systems
Example system using DPA-Q amps and Q-Sys

## Slide 25: QSC Position on Immersive Sound
We support any practical format
Our role is to provide the best possible tools to the exhibitor so that the creative intent of the filmmaker can be realized within the cinema
Our objective is to provide the highest possible quality components and systems for any format, for any size room, within the budget requirements of our end customer

## Slide 26: QSC Cinema Heritage
QSC has been in business over 50 years
Cinema Amplifiers since 1980
  Industry’s leading supplier
Cinema Loudspeakers since 2002

## Slide 27: QSC Processors + QSC Amplifiers + QSC Loudspeakers

## Slide 28: What is ?
Known input/output
Intrinsic Correction™ optimizes loudspeaker performance
Streamlined interconnections that convey more than the signal alone
Complete engineering continuity
  Same team develops all products
  Consistent design approach
One brand, one system - Only from QSC

## Slide 29
Any questions?
thank you