## Slide 1
GPIO
Applications
An attempt to demystify and use the many GPIO variants we have in Q-Sys products
presented by Fred Thomke

## Slide 2
Legacy Cores, type 1 and 2
  1000, 1100
  3000, 3100
  4000
Enterprise Cores
  5200
Integrated Cores
  250i, 500i, 510i, 510c
Unified Core
  110f, 110c
How varied are the GPIO options in Q-Sys?
Cores
I/O Frames, type 1 and 2
  4-card and 8-card
I/O-22
DCIO and DCIO-H (Cinema)
I/O-8 Flex
Page Stations and Expanders
CXD-Q / DPA-Q / CX-Q amps
Peripherals

## Slide 3
Any GPIO in non-Q-Sys devices?
PLD / CXD / DPA amps (non-Q models)
MP-M Mixers
MP-A amps
SPA amps
DataPort amps
OK, these ARE Q-Sys devices, but do have “GPIO”
Other Cinema processors
USL JDS-60 and JDS-100
DPM processors
DCP and DCM processors
Legacy K family speakers
  K8, K10, K12, KSub

## Slide 4
Legacy and Integrated Cores (and I/O-8S)
These Cores have TWO 15-pin D-Sub connectors.
Each connector has eight GPIO pins:
Labeled GPIO-1, GPIO-2, etc.
D-Sub pins are 3, 11, etc.

## Slide 5
4-slot I/O Frames
4-slot IO Frames have the same 15-pin D-Sub connector but only ONE. The pinout is identical to the Core connectors.

## Slide 6
Legacy / Integrated Cores and I/O Frames
Configured as Inputs:
Digital Input (TTL 3.3V)
Potentiometer (10k Ohm, 12V)
Analog Input (0-24V DC, low z)
Contact Closure Input
WCP-1
WCP-2 (3 pins)
Optical Rotary Encoder (2 pins)
Mechanical Rotary Encoder (2 pins)
Configured as Digital Outputs:
3.3V TTL
Open Collector, High Current
PWM/Inverted PWM Outputs (pulse trains)
Dry relay contacts (OUTPUT ONLY!)
ONE relay!
Cores and I/O Frames with this D-Sub connector have self-resetting fuses!
Must reboot the device to reset

## Slide 7
Legacy / Integrated Cores and I/O Frames
As always, the Help file is your friend!
By the way, is this a DA-15, DB-15, D-15, or what???

## Slide 8
Legacy / Integrated Cores and I/O Frames
As always, the Help file is your friend!
By the way, is this a DA-15, DB-15, D-15, or what???
First developed by Cannon in 1952, these are now governed by international IEC 60807-3 / DIN 41652 standards.

## Slide 9
Legacy / Integrated Cores and IO Frames
HIGHLY suggest a breakout board be used, as opposed to solder or crimp-type connectors!
Winford.com
Amazon.com
Make sure: MALE pins and jack screws!

## Slide 10
Core 110f
The Core 110f has more GPIO pins than its larger siblings, but less flexibility with regard to connection options.
16 Inputs:
Digital (TTL 3.3V or Contact Closure sensing)
Analog input (0-24vdc or Raw, with optional pullup to 12v)
Potentiometer (typically a 10k pot) – two or three wire; use 3-wire whenever possible.
16 Outputs:
3.3V TTL
Open Collector, 24v/200 mA max, with pullup to 3.3V
Raw, with optional pullup
Fused (resettable)

## Slide 11
I/O-8 Flex is similar to the Core 110f
The IO-8 Flex GPIO is exactly half the count of the Core 110f, but its capabilities are identical.
8 Inputs:
Digital (TTL 3.3V or Contact Closure sensing)
Analog input (0-24vdc or Raw, with optional pullup to 12v)
Potentiometer (typically a 10k pot) – two or three wire; use 3-wire whenever possible.
8 Outputs:
3.3V TTL
Open Collector, 24v/200 mA max, with pullup to 3.3V
Raw, with optional pullup
Fused (resettable)

## Slide 12
DCIO and DCIO-H
DCIO devices have “Automation Controls”
Inputs:
Six GPI which are TTL (3.3V typ) and/or Contact Closure sensors, via RJ-45
Outputs:
Four sets of relay contacts (NO, NC, C)

## Slide 13
DCIO and DCIO-H
DCIO devices have a Front Panel knob and Mute button which can be assigned
By default, out of the box, the knob and button do nothing until you wire their GPIO pins to a Master gain and Master mute function in the design.

## Slide 14
I/O-22 and Page Stations
The IO-22 is quite a bit reduced in its GPIO capabilities – BE CAREFUL!
8 connections on I/O-22, 4 on Page Stations
Each can be Input or Output, TTL only!
As Digital Out: TTL 3.3V / 2 mA
As Input: Contact closure or TTL
NO analog input or outputs, no potentiometer!
No Raw, no pullups
I/O-22 only:
GPIO-2 can be 48 kHz Sample Clock
GPIO-3 can be 3/6 kHz Vector Clock
GPIO-4 can be 30-120 Hz Frame Clock (intended for Software debug)
Not enough voltage/current to directly drive ANYTHING! No relays, LEDs, etc.

## Slide 15
CXD-Q and DPA-Q Amps
DPA-Q Amps have eight GPIO pins plus 3-pin relay contacts
8 connections
Each can be Input or Output, 3.3v
As Output
  GPIO-1,2,3,4 limited to 5 mA
  GPIO-5,6,7,8 limited to 18 mA (will drive LEDs)
As Input: Analog (pot), Contact Closure, or TTL
NO Open Collector! (use TTL for add’l relays)
No Raw, no pullups
1 – 3.3V Pwr (100 mA MAX)
2 – GPIO-1
3 – GPIO-2
4 – GND
5 – GPIO-3
6 – GPIO-4
7 – GND
8 – GPIO-5
9 – Relay N.O.
10 – Relay COM
11 – Relay N.C.
12 – GND
13 – GPIO-6
14 – GPIO-7
15 – GND
16 – GPIO-8

## Slide 16
I/O-22
NOTE: When sensing a Contact Closure, the IO-22 GPIO as Inputs is ON/True by default when the contacts are OPEN!

## Slide 17
GPIO Examples: Draper Screen Controls
Using a Winford.com TTL-triggered Relay card:

## Slide 18
GPIO Examples: TTL Relays
There are many other brands and relay counts, the technique is the same. Also, it might be better to drive the coil power with an external supply, especially for voltage other than 12v.

## Slide 19
GPIO Examples: Drive relays directly?
Sometimes, integrator does not have time to order “proper” TTL-driven relay boards. They need to get up and running ASAP. Is there an auto parts store nearby? Does their GPIO device support Open Collector?
Have them purchase auto accessory relays, such as used to add 12v accessories (horns, lights, sirens, alarms, etc.). These have industry-standard (“Bosch-style”) wiring, most with pig-tailed connectors. Make sure to use Open Collector for GPIO -- not all devices support this (i.e., CXD-Q and I/O-22).

## Slide 20
GPIO Examples: Drive relays directly?
There are even sealed mountable cases for these relays. Easy to wire and install, more professional look:

## Slide 21
GPIO Examples: Can the GPIO provide the 12v?
“IT DEPENDS!!” -Pat Brown, Syn-Aud-Con
Does GPIO need to provide 12v current for ALL relays, worst-case?
Typically no more than 240mA max. can be sourced from the 12v GPIO pin (this pin is fused/resettable)
Automotive relays typically draw 80-140 mA each
Each GPIO pin, as Open Collector, can “sink” 200 mA (this pin is NOT fused!)
When in doubt, use an external power supply (wall wart), such as from a Wifi router

## Slide 22
GPIO Examples: What about that pesky diode?
“IT DEPENDS!!” -Pat Brown, Syn-Aud-Con
Some relays include an internal diode across coil

## Slide 23
GPIO Examples: What about that pesky diode?
“IT DEPENDS!!” -Pat Brown, Syn-Aud-Con
The GPIO App guide shows a protection diode added across the relay coil:

## Slide 24
GPIO Examples: What about that pesky diode?
“IT DEPENDS!!” -Pat Brown, Syn-Aud-Con
However, all Cores, Frames, and IO-8Flex have built-in protection, so relay diodes are not really necessary

## Slide 25
GPIO Examples: WCP-1 (simple 10k pot)
WCP-1 is detented (stepped) 10k pot. I suggest always wiring as a 3-wire 10k pot, NOT as the “WCP-1” option when given a choice.
Most-common issue is “Why does my pot only work for the upper-half of its travel, and then very quickly get very loud?”
There is nothing special about this pot. ANY 5-50k pot would work in its place, since wiring this way does not measure resistance, it is a voltage divider.
It is also possible to use the WCP-1 as a 10-position “resistor ladder”, which changes in 10% (1k) increments – very rare, but works great with a Control Router.

## Slide 26
GPIO Examples: WCP-2 (BCD encoder)
WCP-2 is a Binary-Coded-Decimal 6-position rotary switch, with three contact outputs and a common. Each output will be on or off based on a binary representation of the knob position, so:
The real magic is in the 3-bit BCD Decoder/Counter (NO scripting, by the way!)
Position 1 is 001
Position 2 is 010
Position 3 is 011
and so on. It IS indeed possible to get position 0 and/or 7 (for eight possible positions) by removing some “stop pins”.

## Slide 27
GPIO Examples: Mechanical / Optical Encoders
We use rotary encoders (typically mechanical) for many of our QSC products already. These are very common devices, quite useful when more than one “knob” is needed to control a single level -- two wall controls, a UCI screen, and an iPhone would ALL stay in-sync with each other!
Only applies to DA-15 GPIO devices. There are other techniques for other GPIO ...

## Slide 28
GPIO Examples: “Encoder-less” gain?
What’s that you say? You don’t have any encoders, or are using some other devices without GPIO Encoder capability? And you can’t use 10k pots because they “fight” each other? No problem!
... and NO SCRIPT!

## Slide 29
GPIO Examples: Mic LED rings & mute buttons?
You MUST check the mic specs!
Determine if mics send or respond to contact closure or TTL signals.
Some mics use phantom power to energize on-board logic
Some mics are simple contact-closure and plain LEDs
Shure MX392 example

## Slide 30
GPIO Examples: Mic LED rings & mute buttons?
Shure MX396 example (2 or 3 element mics)
This is ONE mic “hockey puck” with three elements ...
... GPIO In for Mute switch, and Out for LED control

## Slide 31
GPIO Examples: Mic LED rings & mute buttons?
Shure MX396 example (four 2- or 3-element mics)
Four “hockey pucks”
Any mute button acts as Mute/Unmute for all

## Slide 32
GPIO Examples: Mic LED rings & mute buttons?
Shure MX396 example (four 2- or 3-element mics)
Four “hockey pucks”
Each mute button acts as an independent Mute/Unmute for its mic independently of others
Uses a Master Mute All / Unmute All scheme, either UCI or GPIO triggered (or both!)

## Slide 33
GPIO Examples: Mic LED rings & mute buttons?
Clock Audio (five mic rings)
Uses RJ-45 connectors at mic
Needs 12v power for logic circuit power, not phantom
A Core 110f can power up to 6 mics, but external supply means 8 mics can be accommodated (16 LEDs max)
Mic itself IS phantom powered

## Slide 34
GPIO Examples: What is this “Raw” setting?
Raw is
Typically used for troubleshooting
Not usually left in the “Raw” state
As an Input:
Think of this as a DVM
Some devices have more “ability” than others
DA-15 type presents all possibilities, both input and output
As an Output
Only Core 110f and I/O-8 Flex
DA-15 devices
Core 110f and I/O-8 Flex

## Slide 35
GPIO Examples: GPIO Matrix – Device vs Capabilities
IOU

## Slide 36
GPIO Questions?
The absolute best way to learn our GPIO is to play with it on real hardware. Have a DVM with you, and also a 10k pot, a couple relays, some pushbutton and toggle switches, some LEDs, a handful of resistors. You will be AMAZED at
How versatile these can be
How easy these are to hook up
Interface to lots of stuff: switches, relays, sensors, etc.
How simple circuit or logic adjustments can affect results